## Slide 1: Simple and Fast Interval Assignment Using Nonlinear and Piecewise Linear Objectives
Sandia is a multiprogram laboratory operated by Sandia Corporation, a Lockheed Martin Company, for the United States Department of Energy’s National Nuclear Security Administration under contract DE-AC04-94AL85000.
Scott A. Mitchell
Computing Research
Sandia National Laboratories
International Meshing Roundtable October 2013
20 minute talk, 5 minute questions
Notes: Fraction of work…

## Slide 2: Outline
Problem definition
  a few simple examples of why it is hard
    tradeoffs needed
    may be infeasible
  an infeasible example
Prior approaches
  Linear constraints – good
  Linear objective – not so much IMHO, depending on setting
    Tam & Armstrong concentrates deviations
    Lex min max is slow series of problems
New solution
  Cubic Objective
  Piecewise linear to get integer solution
  Implemented

## Slide 3: Interval Assignment Summary
First known improvement to FEM interval assignment structure since 1997 lexicographic min-max
  Lots of people write new constraints for new schemes, but this is first change to objective (except Graphics community solving related-but-different problem using MIQP)
Implemented in MeshKit, using IPOPT
  scales to thousands of surfaces in nuclear reactor core models
  1997-2013, Cubit runs lex min-max for every quad and hex mesh
  New solution may migrate to Cubit, as Cubit includes MeshKit library
I just relax bend tilt & wave! 
New nonlinear objective function
Finesse integer constraints using L1 minimization of convex piecewise linear approximation
  adapt piecewise, slope
  heuristics for constraint interactions

## Slide 4: Interval Assignment (IA) Problem Definition
Set the number of mesh edges on each curve, such that the owning surfaces and volumes can be meshed according to their schemes.
  compatible interface meshes, e.g. for parallel
  quad and hex meshing
    triangle and tet meshes have trivial constraints
a
c
b
map
e
d
h
g
f
pave
a=b+c
d=e
b+c+f+g+h=even number
all variables integer (e.g. a=4, b=2.5, c=1.5 is not valid)

## Slide 5: Why is Interval Assignment Hard?
What’s the problem?
  hex meshing is a global problem
  quad meshing is a global problem
    for the same reasons,
    but with much weaker constraints
Integrality makes it much harder.
  Discrete problem
  Combinatorial algorithms needed
Sweep same quad mesh
connectivity front and back
Map same curve mesh connectivity
top and bottom. e.g. 3 edges
Unstructured quad meshing:
Each chord enters the quad mesh an even number of times (0 or 2)
so we need an even number of mesh edges on the boundary.
(necessary and topologically sufficient)
Unstructured hex meshing:
Each chord enters the hex mesh an even number of times (0 or 2)
so we need an even number of quads on the boundary.
Plus contractible loops must be even.
(necessary and topologically sufficient)

## Slide 6: Interval Assignment by linear constraints is old
Interval assignment problem form
Linear constraints, linear objective
  Tam & Armstrong 1993
Linear constraints, lexicographic min-max objective
  Mitchell 1997
Fluid flow matching
  Muller-Hanneman 1997
Linear constraints, quadratic objective
  Bommes et al. 2009+
Interval assignment constraints
Volumes with holes
  Shepherd et al.
Midpoint subdivision
Paver
Submapping
Skew control
Automatic Scheme selection
  White & Tautges 2000
Popular to define constraints for new meshing schemes.
Little change to
objective function form
in FEM community 1997—this paper
(But active area in Graphics 2009+)

## Slide 7: Local Constraints
Each surface has local constraints
  depending on scheme (structure)
  depending on user desires (sizing, skew)
map
pave
Goodyear tire
holes line up, smaller than outside
Eloi Ruiz-Gironés
Edge length at least 0.1:
X <= 4
submap
a
b
e
d
c
midpoint subdivision
side1 = a+b
side2 = c+d
side3 = e
side1 <= side2 + side3
side2 <= side1 + side3
side3 <= side2 + side3
curve has at least one edge
x >= 1
a
b
c
d
e
d – e + a + b = c
e <= d + 1
a < c
e < a OR ...
submap

## Slide 8: Mixed-Integer Linear Constraints
Constraints are linear, no high powers such as x2 = y3
Coefficients are typically 1.
Sum-even modeled with artificial variable, 2-coefficient
  sum(xi)=even  sum(xi) = 2z : z is integer
Expressed in matrix form
Inequality and equality are equivalent
  Ax ≥ b  Ax + y = b, y ≥ 0
  Ax = b  Ax ≤ b and Ax ≥ b

## Slide 9: Benefits of Linear Constraints
Feasible region (space of solutions) is convex (possibly unbounded) we have efficient solution algorithms (especially for linear objective)
f’
x*
  Not so easy for integer solutions
  Unless coefficients are cooperative!
2v nearby integer
points. v=#curves

## Slide 10: Global Infeasibility
The global IA problem may be infeasible, meaning no solution exists,
even when each surface can be meshed in isolation.

## Slide 11: Graphics has discovered quad meshes
Designing Quadrangulations with Discrete Harmonic Forms
Yiying Tong, Pierre Alliez, David Cohen-Steiner, and Mathieu Desbrun
ACM/EG Symposium on Geometry Processing 2006, pp. 201-210
Integer-Grid Maps for Reliable Quad Meshing
David Bommes, Marcel Campen, Hans-Christian Ebke, Pierre Alliez, Leif Kobbelt
SIGGRAPH 2013
Disney Animation
(Pixar uses triangles)
Mostly structured quads
on smooth curved surfaces
Key issue is placement of irregular nodes
State of the Art in Quad Meshing
Eurographics STARS 2012

## Slide 12: Graphics has discovered quad meshes including the need for interval assignment
Solved with mixed-integer linear-constraint optimization, series of problems
The placement of irregular nodes is included in the optimization problems
Mixed-Integer Quadrangulation.
David Bommes, Henrik Zimmer, and Leif Kobbelt.
ACM Trans. Graph. (TOG), 28(3):77:1–77:10, July 2009.
commercial
version

## Slide 13: Objectives: user specified sizes
Goal g for each interval
  about g
    each mesh edge should be about 0.1 inches long
  exactly g (not implemented currently)
    I want exactly 8 intervals here
  at least g
    I need at least 6 here
Achieving all of these g, and constraints, may not be possible.
  How do you measure deviations? Relative values?
Autodesk
g = length / 0.1
x ≈ g
g = 6
x ≥ g
g = 8
x = g

## Slide 14: What’s good about linear objectives?
Optimal solutions occur at corners, easy to find.
  if constraint coefficients cooperate, corners are integer solutions. Integer solution for free!
f’
x*

## Slide 15: What’s wrong with linear objectives?
All the deviations are concentrated
  L1 minimization leads to sparsity in the solution
  not a big deal if deviations are small
  could be a big deal if deviations are large
min sum f(xi,gi)
f ≈ (gi/xi) 3 + (xi/gi) 3
g1 = 9
g2 = 9
g3 = 18
x1 = g1 - n1
x2 = g2 - n2
x3 = g3 + p3
Linear Objectives
min sum w1n1 + w2n2 + w3p3
w3 > w1 = w2
no x1 x2 tradeoff
for most solvers
w3 < w1 = w2
x1
x3
x2
or
lex min max (w1n1, w2n2, w3p3)
Non-Linear Objectives

## Slide 16: My Solutions to spread out deviations
1997 Lexicographic min max solve series of linear programs, one per variable = slow.
  Minimize maximum xi-gi. Fix that xi at a nearby integer value, check feasibility, remove it from equations.
    minimize maximum remaining xi-gi, repeat
  Weighted deviations, relative size
    min max pi(xi-gi >0) + ni(gi - xi >0), where pi = 1/gi ni = 1.3/gi
  i.e. assigning x=10 for g=5, is as bad as x=20 for g=10
Today, cubic objective (L3)
  A small series of nearby problems to get integer
  About the same solution as lex min max, depending on problem size
    L∞vs. L3 norm
min sum f(xi,gi)
f ≈ (gi/xi) 3 + (xi/gi) 3
lex min max (w1n1, w2n2, w3p3)

## Slide 17: Cubic Objective
Good: directly measures relative change, (g->x: 4->8 is as bad as 4->2)
Good: no lexicographic min max, single optimization solve spreads deviations
Good: convex objective (plus convex constraints) local optimum is the global optimum
Bad: non-linear objective requires slower algorithms than a linear one, but the difference is less today than in 1997

## Slide 18: Cubic Objective Solution
Non-integer solution usually
4.5
4.5
19
min sum f(xi,gi)
f = (gi/xi-1) 3 or (xi/gi-1) 3
min F = (x1/4.5 - 1) 3 + (x1/4.5 - 1) 3 + (19/x3-1) 3
minimum when F’ = 0 (or extremes xi=1, etc.)
sum of slopes = 0
19
12.8
6.4
6.4
(later problem definitions fix)
6.4
6.4
12.8
relaxed
I have spread out the
deviations, made the major
compromises

## Slide 19: Piecewise Linear Objective
Good: restores integer solutions for free (often)
Bad: explicit variable for every single unit interval = expensive time, memory
Bend at integer points <-> corner at every integer in the higher-dimensional linear problem where each unit interval is a dimension.

## Slide 20: Adaptive Piecewise Linear Objective
For efficiency, just add the bends (pieces) as needed
4.5
4.5
19
6.4
6.4
12.8
relaxed
Delta variable for each interval [k,k+1]
linear slope = weight = f(k+1) – f(k)
Create three intervals: around relaxed x*, beyond it, below it
Solve min sum weighted deltas (linear)
Add more deltas if solution beyond k+1, repeat
*Notional. For the problem on the left the solution is 6,6,12.
A long chain of surfaces from the long curve might lead to the behavior on the left column.

## Slide 21: Adaptive Piecewise Linear Objective
Add the bends (pieces) as needed
Start with two bends, so relaxed solution is in a trough
to avoid unbounded solutions right away

## Slide 22: Tilt to Break Non-integer Ties
Break non-integer ties by tweaking the weights (of the deltas), an additive factor to the slope of the objective.
Randomization helps avoid cases where, say, many variables to the right gang up to motivate a non-integer solution on the left.
Scaling heuristics needed when goals or deviations vary widely,
else small goal variables are left at non-integer values.
Numerical tolerance issue with solvers
e.g.
6.4
6.4
12.8
relaxed
6.5
6.5
13
no tilts
6
6
12
after tilts
=
constraint

## Slide 23: Last Resort, Waves to Force Integrality
unstuck ½ (fractional) integer values
constrain g < 0.001
g(x)
x
x=sum of edges, need an even number
Better, in progress: bends and tilts for sum-even variables
e.g.
6.5
6.5
13
no tilts
6
7
13
after waves
Bad: breaks convexity, local minima are not global minima
IPOPT has limited global optimization capabilities

## Slide 24: Scaling stress tests
scaling by curves
scaling by faces
Time for an integer solution is only a small multiple of the time for the relaxed solution. In contrast, Lex min max grows quadratic+ in problem size
Runtime about O(c1.5) for c variables.

## Slide 25: Robustness stress tests
Problems needing tilts to get integer solutions
“radish”
Split curves provide more degrees of freedom: more tilts are needed to remove fractional values.
Only a few tilts are necessary, tilt for each split curve in the chain is simultaneous.

## Slide 26: Availability and Status
MeshKit algorithm implementation
  Open source
    http://gnep.mcs.anl.gov:8010/meshkit/
  Well defined API
  IPOPT optimization library is free
    MA27 linear algebra library is free
    but you have to download it yourself
    HSL (formerly the Harwell Subroutine Library). A collection of Fortran codes for large scale scientific computation. http://www.hsl.rl.ac.uk, 2011. Includes MA27. IPOPT special instructions at http://www.hsl.rl.ac.uk/ipopt/
To do:
  Robustness and quality testing on large models
  Tilt for sum-even constraints
    better than just waves

## Slide 27: Alternatives
Why bother with the nonlinear solver?
  it is fast, uses little memory
  but maybe you don’t have one
Skip the relaxed cubic-objective phase
  start with piecewise linear adaptive bends
  efficiency would depend on numerics, how far the optimal solution is to the initial goals

## Slide 28: Alternatives
Why sum-of-cubes objective function?
  Any power in [2, infinity] is possible.
    Lex Min Max from 1997 is a form of L_infinity
    The lower the power, the bigger the worst deviation, but the fewer number of curves need to change
  Experimental. I tried powers of 2, 3, and 4.
    2 concentrated deviations too much
    4 spread deviations out too much in some contrived cases
    This was just my opinion
  Some other power may be better, depending on what a “typical” model is for you.

## Slide 29: Interval Assignment Summary
First known improvement to FEM interval assignment structure since 1997 lexicographic min-max
  Lots of people write new constraints for new schemes, but this is first change to objective (except Graphics community solving related-but-different problem using MIQP)
Implemented in MeshKit, using IPOPT
  scales to thousands of surfaces in nuclear reactor core models
  1997-2013, Cubit runs lex min-max for every quad and hex mesh (that meshes the boundary first)
  New solution may migrate to Cubit, as Cubit includes MeshKit library
I just relax bend tilt & wave! 
New nonlinear objective function
Finesse integer constraints using L1 minimization of convex piecewise linear approximation
  adapt piecewise, slope
  heuristics for constraint interactions

## Slide 30: Thanks
It takes a village to make me successful
Thanks to Tim Tautges for suggesting and supporting this project
Thanks to Tim Tautges, Rajeev Jain, for MeshKit
Thanks to Carl Laird, for IPOPT
Thanks to David Bommes for Graphics quads via mixed-integer quadratic programming
This work was funded under the auspices of the Nuclear Energy Advanced Modeling and Simulation (NEAMS) program of the U.S. Department of Energy Office of Nuclear Energy, U.S. Department of Energy. Partial support for this work was provided through Scientific Discovery through Advanced Computing (SciDAC) program funded by U.S. Department of Energy, Office of Science, Advanced Scientific Computing Research. Sandia National Laboratories is a multi-program laboratory managed and operated by Sandia Corporation, a wholly owned subsidiary of Lockheed Martin Corporation, for the U.S. Department of Energy’s National Nuclear Security Administration under contract DE-AC04-94AL85000.
Is the government still shut down? Will mesh for food.